## Slide 1
CI-156L
FEATURE
Professional LED Display System
Indoor Fixed LED Display
www.voatek.com
e-mail : voatek@naver.com
Tel : 031-8011-0388
600 × 337.5mm 다이캐스트 알루미늄 캐비닛 적용, 두께 28mm의 초슬림 디자인
1.56mm 픽셀 피치 지원
16:9 비율 캐비닛 설계, 2K / 4K / 8K 해상도에 최적화된 구성
150 × 337.5mm 대형 모듈 적용으로 높은 평탄도 구현
170° 광시야각, 10,000:1 명암비, ≥3840Hz 주사율, ≥14bit 그레이스케일 지원
모듈 전면 IP65, 방진·산화 방지·정전기 방지·충격 방지 설계
100% 전면 유지보수 지원
벽면 브라켓 설치 또는 바퀴형 스태킹 프레임 설치 지원
전원 공급장치 / 리시빙 카드 이중화 옵션 지원
전원 공급장치와 HUB 일체형 2-in-1 구조
SPECIFICATION (Module)
항목 | 세부내용
Pixel Pitch | 1.5625mm
Pixel Configuration | COB 1R1G1B
Density | 409,600 pixels/㎡
Backshell Material | No Backshell
Module Resolution (L×H) | 96 × 216 pixel
Module Dimension (L×H) | 150 × 337.5 mm
Cabinet Resolution (L×H) | 384 × 216 pixel
Cabinet Dimension (L×H×D) | 600 × 337.5 × 28 mm
Cabinet Material | Die-cast aluminum
Cabinet Weight | ≈3.78kg

## Slide 2
CI-156L
Professional LED Display System
Indoor Fixed LED Display
www.voatek.com
e-mail : voatek@naver.com
Tel : 031-8011-0388
항목 | 세부내용
Brightness | 0-600cd/㎡ adjustable, max brightness ≥1200 cd/㎡
Viewing Angle (Horizontal×Vertical) | 160° × 160° (±10°)
Single Point Color Correction | Standard Configuration
Single Point Brightness Correction | Standard Configuration
Driver IC | Constant Current Drive
Scanning Method | 1/48
Gray Grade | 14bit
Maximum Current (A) | 5
Operation Power | AC 100-240V
Supply Voltage (V) | DC 4.2V
Max. Power Consumption | 350W/㎡
Avg. Power Consumption | 150W/㎡
Frame Frequency | 50-60Hz
Screen Refresh Frequency | ≥3840Hz
Contrast Ratio | ≥10000:1
Chromatic Uniformity | ±0.003Cx, Cy
Color Temperature /Luminance Uniformity | 3000-18000K adjustable；≥98%
Working Temperature | -20℃~+50 ℃
Working Humidity Range | 10-95% RH
Storage Temperature | -40℃~+70 ℃
Storage Humidity Range | 10-95% RH
Lifetime | 100,000 hours
MTBF | 10,000 hours
Protection Grade | IP40 (Module Face IP65)
Installation methods | Front or Back Installation
Maintenance method | Front maintenance
SPECIFICATION (Electricity)