## Slide 1
SI-186L
FEATURE
Professional LED Display System
Indoor Fixed LED Display
www.voatek.com
e-mail : voatek@naver.com
Tel : 031-8011-0388
1.86mm 미세 픽셀 피치 적용으로 정밀하고 선명한 화면 구현
SMD1515 LED 패키지 적용 및 ㎡당 289,000픽셀의 고밀도 디스플레이 구성
다이캐스트 알루미늄 캐비닛 적용으로 견고하면서도 안정적인 구조
DVI, HDMI, SDI, HD-SDI 등 다양한 영상 입력 신호 지원
400~600cd/㎡ 밝기와 수평 140° / 수직 120° 의 넓은 시야각 지원
12~14bit 그레이스케일 및 최대 4.4조 색상 표현
소프트웨어 또는 센서를 통한 100단계 밝기 조절 및 3000~10000K 색온도 조절 지원
이더넷 최대 100m, 광케이블 최대 20km 제어 거리 지원
SPECIFICATION (Module)
항목 | 세부내용
Pixel Pitch | 1.86mm
Pixel Configuration | SMD1515
Density | 289000pixels/㎡
Module Resolution (L×H) | 172 × 86 pixel
Module Dimension (L×H×D) | 320 × 160 ×16.2 mm
Module Quantity in a Cabinet (L×H) | 3 × 2
Cabinet Resolution (L×H) | 344 × 258 pixel
Cabinet Dimension (L×H×D) | 640 × 480 × 62 mm
Cabinet Material | Die-cast aluminum
Cabinet Weight | ≈6.5kg

## Slide 2
SI-186L
Professional LED Display System
Indoor Fixed LED Display
www.voatek.com
e-mail : voatek@naver.com
Tel : 031-8011-0388
SPECIFICATION (Electricity)
항목 | 세부내용
Brightness | 400-600cd/㎡
Viewing Angle (Horizontal×Vertical) | 140° × 120°
Best Viewing Distance | ≥1.8m
Gray Grade | 12-14bits
Display Color | 4.4 trillion colors
Brightness Adjustment | 100 grades by software or automatically by sensor
Operation Power | AC 220-240V, 47-63Hz Switchable
Power Supply | SIQI HT-200-4.5V
Max. Power Consumption | 300W/㎡
Avg. Power Consumption | 100W/㎡
Receiver Card | Novar 7508
Frame Frequency | ≥60Hz
Screen Refresh Frequency | ≤7680Hz
Input Signal | Composite Video, S-video, DVI, HDMI, SDI, HD-SDI
Control Distance | 100M(Ethernetcable) / 20KM(Optical fibercable)
Support VGA Mode | 800×600, 1024×768,1280×1024, 1600×1200
Color Temperature | 3000-10000 adjustable
Brightness Correction | Pixel by pixel, module by module, cabinet by cabinet
Working Temperature | -20~+50 ºC
Storage Temperature | -40~+60 ºC
Working Humidity | 10-90% RH
Lifetime | 100,000 hours
MTBF | 5,000 hours
Continuous Operating Time | ≥72 hours
Protection Grade | IP30
Out-of-Control Pixel Rate | ≤0.01%
Maintenance method | Front and rear maintenance